## Slide 1: DCH alignment and beam momentum
A - mass number;
Z - number of protons;
- beam energy per nucleon;
- proton mass.
P_beam = 7.0 GeV
Pbeam(est)
- angle of beam before magnet (MWPC, Si);
- angles of beam after magnet (DCH);
- magnet field integral [T*m].

## Slide 2: Alignment procedure
Z
DC 1
DC 2
~200 cm
Slopes in both chambers must be equal
The segments extrapolated in z_mid must meet in the same point
Z_mid

## Slide 3: FIRST way
DCH1 fiducial;
DCH2 slope and coords adjusted so two chambers are parallel and the segments are pointing to the same point at z_mid
X2_slope_shift = -0.005 rad;
X2_coordinate_shift = -5.99 cm;
P = 7.68 GeV
P_beam = 7.0 GeV

## Slide 4: SECOND way
As the magnet and DCH were not moved since last data tacking the GEM-DCH alignment for Run7 SRC can be used.
X1_slope_shift = 0.003 rad;
X2_slope_shift = -0.002 rad;
X1_coordinate_shift = 11.26 cm;
X2_coordinate_shift = 5.87 cm;
P = 7.6 GeV
P_beam = 7.0 GeV

## Slide 5: THIRD way
The Beam at 0A is the origin of coordinate system;
DCH1 & DCH2 slopes and coords adjusted in accordance with the beam;

## Slide 6: Slope adjustment
field | intBl | ax_1 | ax_2
0 | 0 | 0,004 | 0,0025
300 | 0,471 | 0,0229 | 0,0181
600 | 0,984 | 0,0415 | 0,0353
900 | 1,455 | 0,0608 | 0,055
1200 | 1,93 | 0,0797 | 0,0757
1600 | 2,55 | 0,1044 | 0,0998
1800 | 2,84 | 0,1161 | 0,1117
Chart: 
| 0.47099999999999997 | 0.98399999999999999 | 1.4550000000000001 | 1.93 | 2.5499999999999998 | 2.84
DCH1 | 0.0229 | 0.0415 | 0.0608 | 0.0797 | 0.1044 | 0.1161
DCH2 | 0.0181 | 0.0353 | 0.055 | 0.0757 | 0.0998 | 0.1117
Chart: 
| 0.47099999999999997 | 0.98399999999999999 | 1.4550000000000001 | 1.93 | 2.5499999999999998 | 2.84
 | 0.0194 | 0.0381 | 0.0575 | 0.0765 | 0.1009 | 0.1128
 | 0.0204 | 0.0379 | 0.0574 | 0.079 | 0.1023 | 0.114
After few iterations the free coef is ~0
X1_slope_shift = 0.0034 rad;
X2_slope_shift = -0.0023 rad;
Initial slopes w/o alignment

## Slide 7: Coordinate adjustment
With new slopes we looked at segment coords in z_mid
field | intBl | x_1 | x_2
0 | 0 |  | 
300 | 0,471 | -19,96 | -18,66
600 | 0,984 | -25,64 | -27,38
900 | 1,455 | -33,2 | -39,5
1200 | 1,93 | -40,42 | -51,1
1600 | 2,55 | -49,88 | -64,74
1800 | 2,84 |  | 
Chart: 
| 0.47099999999999997 | 0.98399999999999999 | 1.4550000000000001 | 1.93 | 2.5499999999999998
 | -19.96 | -25.64 | -33.2 | -40.42 | -49.88
 | -18.66 | -27.38 | -39.5 | -51.1 | -64.74
X1_coord_shift = -12.20 cm;
X2_coord_shift = -6.74 cm;
Automaticaly made the global DCH slope (x2-x1/dz) equal with local slopes, i.e. for 1800A run ax1=ax2=ax_gl=0.1136 rad

## Slide 8: Beam momentum estimation procedure
Pbeam(est)
- angle of beam before magnet (MWPC);
- angles of beam after magnet (DCH);
- magnet field integral [T*m].
A - mass number;
Z - number of protons;
- beam energy per nucleon;
- proton mass.
P_beam = 7.0 GeV
With third way alignment corrections we have:
600A P = 7.587 GeV, σ = .68 GeV, ) = 0.0035
900A P = 7.408 GeV, σ = .46 GeV, ) = 0.0037
1200A P = 7.443 GeV, σ = .33 GeV, ) = 0.004
1600A P = 7.532 GeV, σ = .24 GeV, ) = 0.007
1800A P = 7.526 GeV, σ = .22 GeV, ) = 0.008
) must be CONSTANT

## Slide 9: Conclusions and possible ways
Nominal Nuclotron beam momentum or energy are given wrong;
The alignment with upstream tracks can give a better picture of alpha_in;
The simplest way is to leave FIRST way alignment and to adjust it later if needed

## Slide 10: Run6 Momentum vs. Int(BdL)
RED – Nuclotron beam momentum;
BLUE – estimated beam momentum.
A - mass number;
Z - number of protons;
- beam energy per nucleon;
- proton mass.
Pbeam(est)
C beam energy 4.5 GeV/nuclon;
Momentum 10.7 GeV/c;